## Slide 1: GeoFluids 2020
Peter Flemings
Jack Germaine
Maria Nikolinakou

## Slide 2
Agenda:
8:00-8:30: Arrival and security check 8:15-9:00: Coffee with pastries 9:00-9:15: UT GeoFluids Proposal Overview - Flemings
9:15-9:45: Experimental Plan followed by Q&A: Germaine 9:45-10:15: Poromechanical Plan followed by Q&A: Nikolinakou 10:15-10:30: Break
10:30-11:00: Field Studies Plan followed by Q&A: Flemings
11:00-11:10: Bureaucratic details - Flemings 11:10-11:30: Discussion

## Slide 3: http://www-udc.ig.utexas.edu/geofluids/aboutus.php
UT GeoFluids 2020 proposal

## Slide 4
10 year program (2019-2028)
  1st payment May 2019
  no cost to terminate
  After 2019, 1 year buy-in
Led by University of Texas (Institute for Geophysics) - partnered with Tufts University
Cost: Initiate at $50,000, increment at 2% per year.
Overview

## Slide 5
Pore pressure prediction has been largely empirical and reliant on ‘uniaxial’ approach. However, the discipline is on the edge of a more holistic approach.
We the full stress tensor to complex soil behavior to predict stress and pressure. We incorporate this approach in workflows and apply it to field studies.
We are developing a unified approach that incorporates stress dependency, creep, and loading path to predict pressure and stress.
We already see evidence that this unified approach improves well design and provide insight into geological processes. These advances will expand.
What do we do?

## Slide 6
In 2009, a conceptual vision: the incorporation of geomechanics, through integration of experiment, theory and field observation, would lead to advances in pore pressure and stress prediction
2009 vs. 2018 2019 vs. 2028!
2009- Vague Concept that full stress tensor matters
Drilling window, s3-u (ppg)
Systematic approach to couple seismic velocity to geomechanical models for pore pressure prediction

## Slide 7
  Experimental: Analyze fabric, acoustic, electrical, and material properties of mudrocks : 0.1-100 MPa.
  Poromechanical Modeling: Develop/apply coupled models to link realistic rheologies, deformation, stress (shear and normal), and pore pressure.
  Field Study: Analyze pore pressure, stress, deformation in thrust belts and in the sub-salt.
Study the state and evolution of pressure, stress, deformation and fluid migration through experiments, models, and field study. Produce innovative concepts that couple geology and fluid flow.
UT GeoFluids Research: couple geology and fluid flow

## Slide 8
Research goals

## Slide 9
2.1 Experimental studies

## Slide 10: Outline: Experimental Program
UT GeoFluids achievements in mudrock behavior
  Resedimentation technology
  Fundamental trends with stress level and lithology
UT GeoFluids 2020 proposed research:
  Proposal section 2.1.2: Resedimented vs Intact
  Proposal section 2.1.3: Generalized loading effects
  Proposal section 2.1.4: Wave velocity characterization
  Proposal section 2.1.5: Visco-plastic effects

## Slide 11: Experimental Overview
Stress range 0.1 to 100 MPa
  1 – 1000 TSF
  14.5 -14,500 psi
13 different materials
Resedimented Specimens
Physical characteristics
  PSD, CEC, SSA, liquid limit
  Mineralogy, microfabric
Mechanical Properties
  Permeability, compressibility, strength
  Velocity, resistivity

## Slide 12: Primary Materials Under Investigation
Abbreviation | Name | Source
RBBC | Boston Blue Clay | Excavation
RGoM-EI | Gulf of Mexico - Eugene Island Block | Core
RGoM-Ursa | Gulf of Mexico - Ursa | Core
RSFBM | San Francisco Bay Mud | Core
RLC | London Clay | Core
RPC | Presumpscot Clay | Core
RNC | Nankai Clay | Core
RUC | Ugnu Clay | Core
SS | Skibbereen Silt | Core
RK-Cornwall | Cornwall Kaolin | Mined
RK-EPK | Edgar Plastic Kaolin | Mined
RK-VTK | Villanova Tulo White Kaolin | Mined
Illite | Illite | Mined
R prefix in abbreviation indicates Resedimentation
Notes: 13 materials

## Slide 13: Plasticity Distribution of Test Materials
Chart: Liquid Limit, wL
| 0 | 7 | 14 | 21 | 28 | 35 | 50 | 50 | 126
A line | -14.6 | -9.49 | -4.38 | 0.73 | 5.84 | 10.95 | 21.9 | 21.9 | 77.38
Uline | -7.2 | -0.9 | 5.4 | 11.7 | 18 | 24.3 | 37.8 | 37.8 | 106.2
50 Line | 0 | 50
RBBC | 22.7
RGoM-EI | 63
RGoM-Ursa | 28
RK-Cornwall | 19
RK-EPK | 31
RK-VTK | 15
RLC | 43.3
RNC | 39
RPC | 13.7
Notes: 3 kaolins below A line
Focus on BBC, Ssilt, Uras, London, Eug Isl
Extensive range

## Slide 14: Resedimentation from Natural Samples
Maintains natural complexity
Uniform test specimens
Controlled formation history
  Fabric, density, and stress
Controlled composition
  PSD, mineralogy, pore chemistry
Unlimited supply
No sample disturbance

## Slide 15: Grind to Fine Powder
Method depends on quantity
  Mortar and pestle
  Ball mill
  Rotary disc grinder
99% passing #100 sieve
Does not break particles
Not likely to destroy clay flocs
Resedimentation Method
Notes: Flocs persist because leaching causes different behavior

## Slide 16: Mix Individual Batches
Blend ingredients
Temper to hydrate particles
Evacuate to remove air
Tremie into rigid walled cylinder
Resedimentation Method

## Slide 17: Incrementally Consolidate
Floating ring geometry
Load at EOP
LIR = 1
Secondary at max stress
Unload to OCR = 4 to 5
Extrude sample
Resedimentation Method

## Slide 18: Equipment for Uniaxial Compression Testing
Low Stress < 12 MPa
Medium Stress < 40 MPa
High Stress <100 MPa
Measure:
Permeability
Compressibility

## Slide 19: Typical Permeability Behavior
Chart: Porosity, n
| 0.58150000000000002 | 0.57389999999999997 | 0.55889999999999995 | 0.54110000000000003 | 0.52229999999999999 | 0.49340000000000001 | 0.46700000000000003 | 0.4476 | 0.43659999999999999 | 0.4264 | 0.40679999999999999 | 0.3866 | 0.5988 | 0.58609999999999995 | 0.56910000000000005 | 0.54949999999999999 | 0.52669999999999995 | 0.49309999999999998 | 0.46450000000000002 | 0.44679999999999997 | 0.43690000000000001 | 0.42730000000000001 | 0.40749999999999997 | 0.38590000000000002
R. Presumpscot Clay (RPC) | 1.1848e-15 | 5.2647e-16 | 8.4466e-16 | 4.6109e-16 | 4.3499e-16 | 4.2893e-16 | 9.3016e-17 | 8.2829e-17 | 4.618e-17 | 4.3824e-17 | 3.6863e-17 | 1.3649e-15 | 7.0156e-16 | 7.2777e-16 | 4.1286e-16 | 4.6226e-16 | 9.8479e-17 | 8.0834e-17 | 5.5763e-17 | 6.2966e-17 | 4.8975e-17
R. Boston Blue Clay (RBBC) | 2.2425e-15 | 7.6777e-16 | 5.0804e-16 | 3.275e-16 | 1.2397e-16 | 3.8713e-17 | 2.5644e-17 | 2.9471e-17 | 1.7615e-17 | 1.6297e-16 | 1.0453e-16 | 7.5294e-17 | 4.4162e-17 | 2.1579e-17 | 2.0745e-17 | 2.7575e-15 | 1.2788e-15 | 1.0473e-15 | 1.2238e-15 | 7.9271e-16 | 6.2054e-16 | 1.4223e-16 | 4.9314e-17 | 9.7123e-16 | 1.0926e-15 | 6.2478e-16 | 5.7037e-16 | 1.383e-16 | 5.3463e-17 | 3.3687e-17 | 2.1939e-17 | 1.7332e-17
R. London Clay (RLC) | 2.7481e-15 | 9.024e-16 | 7.4748e-16 | 1.1263e-15 | 4.88e-16 | 2.1627e-16 | 7.3743e-17 | 3.5432e-17 | 7.9208e-18 | 5.3579e-16 | 2.5767e-16 | 1.5142e-16 | 5.8997e-17 | 1.0822e-17 | 4.1707e-18 | 9.9949e-19
Increasing wL
1 cm/sec =᷉ 10 -9 m2
Notes: -16 is equal to 10-7 cm/s
Need to change this over to EI

## Slide 20: Uniaxial Compression Behavior
Chart: Vertical Effective Stress 'v (MPa)
1 MPa =᷉ 10 TSF
Notes: Slopes different shape and position
Sensitive to type at low stress
Not much difference at high stress
Will require different model formulations

## Slide 21: Equipment for Triaxial Shear Testing
< 12 MPa
< 40 MPa
<100 MPa
Measure:
Compression
Lateral Stress Ratio
Undrained Strength
Friction Angle
Basic Design

## Slide 22: Variation in K0,NC with Stress and Composition
Chart: Vertical Effective Stress, σ'v (MPa)
| 101.25
RBBC single | 0.595
R. Boston Blue Clay | 0.557 | 0.521 | 0.601 | 0.493 | 0.554 | 0.557 | 0.581 | 0.525 | 0.532 | 0.517 | 0.492 | 0.557 | 0.495 | 0.55 | 0.58558 | 0.585 | 0.556 | 0.57983 | 0.577 | 0.595 | 0.605
R. GoM Eugene Is | 0.655 | 0.698 | 0.805 | 0.619 | 0.626 | 0.828 | 0.917 | 0.844 | 0.595 | 0.68 | 0.649
RBBC trendline | 0.48819 | 0.49776 | 0.50344 | 0.50751 | 0.51069 | 0.51331 | 0.51553 | 0.51746 | 0.51917 | 0.5207 | 0.5309 | 0.53697 | 0.54131 | 0.5447 | 0.54749 | 0.54986 | 0.55192 | 0.55374 | 0.55538 | 0.56626 | 0.57273 | 0.57736 | 0.58098 | 0.58395 | 0.58648 | 0.58867 | 0.59062 | 0.59236
Gom trendline | 0.58322 | 0.61286 | 0.63088 | 0.644 | 0.65435 | 0.66294 | 0.67029 | 0.67672 | 0.68244 | 0.6876 | 0.72254 | 0.74379 | 0.75925 | 0.77146 | 0.78158 | 0.79024 | 0.79782 | 0.80457 | 0.81065 | 0.85184 | 0.8769 | 0.89512 | 0.90952 | 0.92145 | 0.93167
K0,NC = K0,10(0.1σ’v [MPa])J
K0,10
J
Log K0,NC
Log σ‘v
1 MPa =᷉ 10 TSF
Notes: Considerable variation with BBC
Severe increase with GoM
GoM is consistent with
Intercept at 10 MPA
Trends cross but are ordered in this stress range
Exponent J

## Slide 23: Triaxial Compression Undrained Shear - RBBC
0.15
Chart: Axial Strain, ea (%)
s’vc
10 MPa
8.0
6.0
4.0
2.0
0.5
1.0
3
Normally consolidated after Ko compression
(MPa)

## Slide 24: Normalized stress strain curves
Divide stresses by consolidation stress
Finite starting shear stress
Definite peak
With stress
  Lower strength
  Increased strain
  Less softening
Triaxial Compression Undrained Shear - RBBC
0.15 MPa
10 MPa
Stress Level

## Slide 25: Triaxial Compression Undrained Shear - RBBC
Normalized Stress Paths
Stress Level
p’=(s’a+s’r)/2
Lateral Stress Ratio
Friction Angle
Undrained Strength Ratio

## Slide 26: Normally Consolidated Shearing Friction Angle
Chart: Preconsolidation Stress, σ'p (MPa)
| 0.34599999999999997 | 0.96399999999999997 | 0.14199999999999999 | 0.47799999999999998 | 0.81699999999999995 | 0.67 | 0.189 | 0.33200000000000002 | 0.97199999999999998 | 5.87 | 1.954 | 3.9079999999999999 | 7.8220000000000001 | 9.7430000000000003 | 9.8119999999999994 | 5.87 | 0.55700000000000005 | 9.5670000000000002 | 0.55500000000000005 | 0.56299999999999994 | 0.629 | 0.57199999999999995 | 0.58699999999999997 | 9.61 | 20.05 | 40.53 | 101.25 | 5.8570000000000002 | 0.28100000000000003 | 0.27500000000000002 | 0.52300000000000002 | 0.65500000000000003 | 0.45200000000000001
R.Boston Blue Clay | 35.52 | 32.14 | 39.39 | 33.53 | 32.37 | 32.41 | 36.42 | 34.22 | 31.03 | 29.16 | 30.98 | 30.26 | 29.46 | 29.22 | 30.4 | 30.1 | 31.7 | 28.7 | 34.8 | 34.8 | 31.6 | 33.9 | 33.1 | 30.8309 | 29.156 | 28.979 | 26.6 | 30.1 | 33.99 | 32.89 | 0 | 31.5 | 32.2
R. GoM Eugene Is. | 22.76 | 20.22 | 13.56 | 26.85 | 23.87 | 28.3 | 28.2 | 11.545 | 14.4 | 26.7 | 23.2 | 11.9183 | 26.1 | 14.3
GoM trendline | 29.5978 | 26.5091 | 24.854 | 23.7428 | 22.9152 | 22.2604 | 21.7214 | 21.2651 | 20.8706 | 20.5239 | 18.3821 | 17.2344 | 16.4639 | 15.89 | 15.4359 | 15.0622 | 14.7458 | 14.4722 | 14.2318 | 12.7466 | 11.9508 | 11.4165 | 11.0185 | 10.7037 | 10.4445
 | 36.0374 | 34.9549 | 34.3368 | 33.905 | 33.5737 | 33.3054 | 33.0803 | 32.8865 | 32.7165 | 32.5652 | 31.587 | 31.0285 | 30.6382 | 30.3388 | 30.0964 | 29.893 | 29.7179 | 29.5643 | 29.4275 | 28.5436 | 28.0389 | 27.6862 | 27.4157 | 27.1966 | 27.0128 | 26.8545 | 26.7157 | 26.5922
φ’cs = A(0.001σ’p [MPa])B
A
B
Log φ’
Log σ’p
A @ 1000 MPa
1 MPa =᷉ 10 TSF

## Slide 27
Proposed Research
UT GeoFluids Proposal
Section 2.1

## Slide 28: Example: Resed. Vs. Intact Permeability Behavior
Chart: Predicted Permeability (m2)
| 1.1804142928174954E-14 | 4.5846317682482864E-15 | 1.780633170771086E-15 | 6.9158323920565325E-16 | 2.686052268379733E-16 | 1.0432405500102642E-16 | 4.051860263472221E-17 | 1.5737091119151313E-17 | 6.1121564118364624E-18 | 2.373911145325347E-18 | 9.2200751194562938E-19
RBBC | 7.5466e-15 | 2.8927e-15 | 1.1088e-15 | 4.2501e-16 | 1.6291e-16 | 6.2445e-17 | 2.3936e-17 | 9.1749e-18 | 3.5168e-18 | 1.348e-18 | 5.1671e-19
RGOM-Ursa | 8.4314e-16 | 3.2889e-16 | 1.2829e-16 | 5.0044e-17 | 1.9521e-17 | 7.6147e-18 | 2.9703e-18 | 1.1586e-18 | 4.5196e-19 | 1.763e-19 | 6.877e-20
RGOM-EI | 6.1624e-16 | 1.7073e-16 | 4.7299e-17 | 1.3104e-17 | 3.6304e-18 | 1.0058e-18 | 2.7864e-19 | 7.7197e-20 | 2.1387e-20 | 5.9252e-21
RGoM_Lower | 2e-20 | 2e-14
RGOM-Upper | 5e-19 | 5e-13
RGoM-A | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RGoM-B | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RSBM | 1.1934e-15 | 4.3361e-16 | 1.5754e-16 | 5.724e-17 | 2.0797e-17 | 7.5561e-18 | 2.7454e-18 | 9.9747e-19 | 3.6241e-19 | 1.3167e-19
RUC | 4.0841e-15 | 1.3473e-15 | 4.4443e-16 | 1.4661e-16 | 4.8362e-17 | 1.5953e-17 | 5.2626e-18 | 1.736e-18 | 5.7266e-19 | 1.8891e-19 | 6.2316e-20
RPC | 1.2196e-15 | 5.4809e-16 | 2.4632e-16 | 1.107e-16 | 4.9751e-17 | 2.2359e-17 | 1.0048e-17 | 4.516e-18
SS | 1.6181e-14 | 6.8865e-15 | 2.9309e-15
RNC | 5.781e-17 | 1.5977e-17 | 4.4157e-18 | 1.2204e-18 | 3.3729e-19 | 9.3218e-20 | 2.5763e-20
1 cm/sec =᷉ 10 -9 m2
K measured in lab
  CRS test
K predicted from
  Liquid Limit
  initial porosity
  Proposal section 2.1.2: Resedimented vs Intact

## Slide 29: Intact Core Provided by Chevron
Strongly Layered
Extensive separation cracks
Considerable fine sand content
Little clay size
Weakly lithified
  Proposal section 2.1.2: Resedimented vs Intact

## Slide 30
We will:
  Measure site specific resedimentation behavior
  Compare field vs resedimented compression behavior
  Compare laboratory TX shear results
  Compare laboratory velocity results
This requires sponsor support to provide:
  Field compression data
  Intact core
  Proposal section 2.1.2: Resedimented vs Intact

## Slide 31: Field Example: Fold and Thrust Belt Systems
b. Far Field Stress Conditions
Uniaxal compression
Major stress is vertical
Intermediate equals minor
c. Inner Prism Stress Conditions
Plane strain compression
Major stress is horizontal
Intermediate about average
(Flemings and Saffer, JGR, 2018)
  Proposal section 2.1.3: Generalized loading effects

## Slide 32: Laboratory Capabilities
Intermediate Principal Stress
b = (s2 - s3) / (s1 - s3)
0 90
Major Principal Stress Direction
q (degrees from vertical)
0
1
Behavior Depends on:
  Initial (equilibrated) stress state
  Direction of loading relative to deposition
  Relative value of intermediate stress
  Proposal section 2.1.3: Generalized loading effects

## Slide 33
  Proposal section 2.1.3: Generalized loading effects
Loading Conditions Change Yield Surface

## Slide 34
We will:
  Measure the shape of the yield surface
    Using TX stress space
    Following uniaxial compression
    Up to 100 MPa
  Measure the yield surface rotation
    Due to non-uniaxial compression
  Develop capability to independently control the intermediate principal stress
  Proposal section 2.1.3: Generalized loading effects

## Slide 35
Characterization of TI Elastic Stiffness
Vertical Velocities
Inclined Velocity
Horizontal Velocities
Top to bottom
Side to side
Side to top
Vertical Axis of Symmetry
  Proposal 2.1.4: Wave velocity characterization
Notes: Explain how to get each element and for which ones we need horizontal and diagonal velocities

## Slide 36: Wave Velocity Technology
Piezo ceramic crystals
Cylindrical triaxial specimen
Large deformation capability
10 MPa Pressure capacity
Horizontal Actuators
8 cm
P Sender
P Receiver
Soil Specimen
S Receiver
3 cm
2 cm
S Sender
Vertical Actuators
P&S Receivers
  Proposal 2.1.4: Wave velocity characterization

## Slide 37: Velocity Variation with Direction
Chart: Inclination Angle from the Vertical, θ (Degrees)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90
Compressional wave | 2066 | 2068.4726 | 2075.7195 | 2087.2551 | 2102.3497 | 2120.1252 | 2139.6509 | 2160.0243 | 2180.4279 | 2200.1635 | 2218.667 | 2235.5083 | 2250.3817 | 2263.0892 | 2273.5192 | 2281.6243 | 2287.3973 | 2290.8509 | 2292
Shear Wave in xz plane | 442 | 438.888 | 429.892 | 416.008 | 398.8211 | 380.3945 | 363.099 | 349.3419 | 341.1664 | 339.7862 | 345.2603 | 356.5192 | 371.7299 | 388.7733 | 405.618 | 420.5262 | 432.1376 | 439.4868 | 442
Shear wave in xy plane | 442 | 442.4778 | 443.8937 | 446.1961 | 449.302 | 453.1017 | 457.4639 | 462.2424 | 467.2814 | 472.422 | 477.5072 | 482.3868 | 486.9207 | 490.9826 | 494.462 | 497.2666 | 499.3229 | 500.578 | 501
Measured Vpi
Measured Vpv
Measured Vph
Measured Vsv
Measured Vsh
Uniaxial Compression
5 measurements at each stress state
RGoM-EI at 5.6 MPa
  Proposal 2.1.4: Wave velocity characterization

## Slide 38: Proposal 2.1.4: Wave velocity characterization
We will:
  Measure the wave velocity anisotropy during:
    Uniaxial compression
    General drained loading
    Undrained shearing
    Up to 100 MPa
  Develop new capability
    Measure velocity anisotropy at 100 MPa

## Slide 39
  Proposal section 2.1.5: Visco-plastic effects
Continued densification under constant effective stress
Continued reduction in effective stress under constant volume
Creep per log cycle of time is 1 to 5 % of compression slope
Uniaxial Compression

## Slide 40: Proposal section 2.1.5: Visco-plastic effects
We will:
  Measure the time dependent compression:
    Using constant rate of strain 1D tests
    Incremental loading 1D tests
    TX tests with lateral stress measurements
  Measure the time dependent stress relaxation:
    TX tests
    Undrained shearing
    Drained shearing
  Testing will focus on the 5 to 100 MPa range

## Slide 41
Research goals

## Slide 42: Questions

## Slide 43
2.2 Poromechanical Modeling

## Slide 44
Outline
UT GeoFluids achievements in poromechnical modeling
  Static models
  Evolutionary models
UT GeoFluids 2020 proposed research plan for poromechanics:
  Proposal section 2.2.2: Incorporation of experimental observations (e.g., stress level dependency)
  Proposal section 2.2.3: 3D poromechanical modeling
  Proposal section 2.2.4: Couple poromechanical results with reflection seismology to improve pressure prediction as well as imaging

## Slide 45
Elastoplastic mudrock models
Critical state soil mechanics.
Contribution of mean and differential stress to compaction and pore-pressure.
Fundamental attribute of UT GeoFluids research.
Notes: Various presentations and workshops
Importance to advancement of the field

## Slide 46
Static poromechanical models
Heidari et al; Geophysics; in press
Static models
Represent present-day geometry
Allow poromechanical study of specific geologic systems

## Slide 47
Coupling velocities with static poromechanical models
Heidari et al; Geophysics; in press
We developed a workflow to couple static poromechanical models with seismic velocities to enhance pressure and stress prediction
+
Seismic data: Courtesy of BP

## Slide 48
Static models cannot capture the stress and pore pressure history associated with the evolution of the geologic system
Rowan et al, AAPG 2016
Static model of diapir
Static poromechanical models

## Slide 49
Evolutionary poromechanical model
3 km
Evolutionary poromechanical models couple salt flow with deposition and porous fluid flow
They predict how stress, pressure, strength, porosity evolve with time
Nikolinakou et al, 2018, JMPG

## Slide 50
Evolutionary vs. static poromechanical models
Evolutionary models can incorporate stress and strain changes associated with the geologic history (Nikolinakou et al, 2014b, JMPG)

## Slide 51
Evolutionary vs. static poromechanical models
Static models may not be able to identify hazardous drilling zones (Nikolinakou et al, 2014b, JMPG)
B) STATIC
A) EVOLUTIONARY

## Slide 52
Evolutionary models: deformation patterns
Sedimentation and shortening history affect deformation patterns:
Thrust zones
vs.
Coherent folds
Nikolinakou et al, 2018, ARMA

## Slide 53
Stress changes related to salt-system evolution
mean
stress
350
175
0
Local increase in mean stress and decrease in porosity near a source-layer weld
Heidari et al, 2016, Tectonophysics

## Slide 54
Practical implications: Drilling window
High pore pressure
Low minimum principal
Minimal drilling window subsalt
l* = 1: Pore pressure on lithostat
l* = 0: Pore pressure on hydrostat
}

## Slide 55
No sand layer
Sand layer
Excess pressure (MPa)
80
40
0
3 km
40 m.y.
Presence of sand (permeable) layer
Sand layers allow for excess pressure transmission towards salt
 Higher pore pressures near salt wall
More complete models that couple salt flow and fluid flow to stress and strength predict fundamentally different geologic behavior
Heidari et el, 2017, ARMA

## Slide 56
Mechanics of thrust belts
Gao et al, 2018, JGR
20 km
VE =1
Trench
Overpressure (MPa)
Transient models couple tectonic loading with porous fluid flow and predict overpressure and stress in both hanging wall and footwall.

## Slide 57
Mechanics of thrust belts
Poromechanical models of thrust belts quantify the contribution of mean and shear stress to porosity loss
Gao et al, 2018, JGR
Notes: Trace the evolution of the strain ellipse

## Slide 58
UT GeoFluids 2020 Proposal
Section 2.2: Poromechanical studies

## Slide 59
Traditional constitutive models:
Stress ratio, friction angle: constant
Orders of magnitude difference
in scale and stress level
Proposal section 2.2.2: Incorporate more realistic behavior
Notes: Not clear if our constitutive model assumptions still apply
More realistic material behavior for these geologic scales

## Slide 60
We will develop a constitutive model that incorporates:
stress-level dependency of frictional strength, undrained strength and stress ratio;
the asymmetry (rotation) and evolution of the yield surface under complex geologic loading and high stress levels;
stress-strain rate sensitivity.
Output: numerical models with more realistic material description
Proposal section 2.2.2: Incorporate more realistic behavior

## Slide 61
Effective stress ratio increases with confining stress
Friction angle decreases with confining stress
Casey et al; JGR 2016
Proposal section 2.2.2: Stress dependency
Casey at al, 2016, JGR
Notes: Experimental work; Dramatic change in material properties
Empirically observed, now measured
Input for models; borehole stability analyses

## Slide 62
We are incorporating stress level dependency into numerical models.
We predict fundamentally different stress distributions
Proposal section 2.2.2: Stress dependency

## Slide 63
Proposal section 2.2.2: Stress dependency
We are developing an enhanced critical state model that builds on our experimental findings.
Heidari at al, 2018, ARMA

## Slide 64
Shape of yield and iso-porosity surface greatly impacts model behavior, stress and pressure prediction
❓
❓
Proposal section 2.2.2: Yield surface shape & rotation
Notes: Here symmetric
Next issue: yield surface: how does it look like and ho does it evolve in high stress stress levels and complex stress paths
Examples: we are probing yield surface for GoM material; we are exploring how the yield surface evolves in complex stress paths
Cutting edge problem + how to incorporate behavior in models; make it accessible for industry workflows

## Slide 65
Proposal section 2.2.3: 3D modeling of salt systems
Need to incorporate the complexity of the 3D salt geometries in poromechanical modeling.
Salt system offshore West Africa, (courtesy of Repsol)

## Slide 66
Develop static 3-dimensional models and study the effect of complex geometries to stress and pressure.
Explore evolutionary 3-dimensional models.
Build models of actual salt bodies and evaluate our poromechanical results with available data.
Provide criteria and guidelines for investing in a 3D studies.
Proposal section 2.2.3: 3D modeling of salt systems
Notes: Plane-strain or axisymmetric models cannot capture complex 3D salt geometries.

## Slide 67
Proposal 2.2.4: Link stress/pressure to seismic imaging
Approach based on evolutionary models
Final porosity, pore pressure and stress
Bedding orientation and strain evolution
Elastoplastic moduli
Anisotropic velocity (CIG) models
Synthetic shot gathers
Synthetic seismic image
Signature of stress and pressure on seismic imaging
Improve seismic analysis tools
Kyle Spikes and Mrinal Sen
Notes: Entire stress/strain history and elastoplastic stress description; bedding information; porosity
Gain insights on how stress and pressure are recorded on seismic data
This is a forward approach

## Slide 68
Proposal 2.2.4: Link stress/pressure to seismic imaging Approach based on field data and static models
Compare with measured data
Re-define salt shape
Signature of stress on seismic imaging
Improve seismic tools
Direct stress inversion
Anisotropic velocity (CIG) models
Synthetic shot gathers
Synthetic
seismic
image
Kyle Spikes and Mrinal Sen

## Slide 69
Proposal 2.2.4: Rock physics models
(Spikes & Sen)
Rock physics approaches to calculate stiffness tensor:
Empirical relationships derived from laboratory measurements
Perturbations of a background velocity with anisotropic considerations constrained by laboratory measurements
Third-order elasticity constrained by laboratory measurements
Kyle Spikes and Mrinal Sen
Notes: A fundamental challenge: how to incorporate the poromechanical results into rock physics models

## Slide 70
Proposal section 2.2: Poromechanics - Key points
  We will incorporate experimental observations into numerical analyses (e.g., stress level dependency).
  We will build 3D poromechanical models to study the effect of salt geometry on stress and pressure.
  We will create couple poromechanical results with reflection seismology to improve pressure and stress prediction as well as imaging.

## Slide 71
Research goals

## Slide 72
2.3 Field study

## Slide 73
Outline
UT GeoFluids achievements in Field Studies
  Coupling velocity data with geomechanical modeling for pressure & stress prediction
  Flow Focusing
  Salt Systems
  Thrust Belts
UT GeoFluids 2020 proposed research plan for field studies:
  Proposal section 2.3.2: Validation of pormechanical predictions with field study (e.g., stress level dependency)
  Proposal section 2.3.3: Validation of pressure prediction workflows

## Slide 74
Pore pressure ()
Mean effective stress ()
Achievements in Field Studies: FES method
Mean total stress ()
Velocity variation with equivalent stress
Geomechanical modeling
Iso-velocity contours*
Shear stress ()

## Slide 75
Achievements in Field Studies:
Coupling velocity data with geomechanical modeling for pressure & stress prediction (Heidari et al., in press)

## Slide 76: Achievements in Field Studies: Flow Focusing

## Slide 77: Achievements in Field Studies: Flow Focusing

## Slide 78: Achievements in Field Studies: Flow Focusing

## Slide 79: Achievements in Field Studies: Flow Focusing
Gao and Flemings (2017)
Flemings & Lupa(2004)
Estimate reservoir pressure from mudstone pressure, reservoir geometry, and mudstone permeability

## Slide 80
Pore pressure of Q sand converges on the overburden
Achievements in Field Studies: Flow Focusing
Field Tested the Protected Trap Concept
Trap Integrity Map

## Slide 81: Achievements in Field Studies: Flow Focusing Pressure regression in Macondo
A’
A

## Slide 82: Achievements in Field Studies: Salt Systems Testing workflows
Heidari et al; Geophysics; in press

## Slide 83
Achievements in Field Studies: Salt Systems
Quantify Mean & Shear Induced Pressures
Approach:
Document pressure and stress in salt systems
compared pressure & stress predictions with field data
Notes: - I’ll explain what is driving these differences.

## Slide 84: Achievements in Field Studies: Thrust Belts
Incorporate complex stress state for pressure and stress prediction
Applied in Nankai Trough
Flemings and Saffer, 2018

## Slide 85: UT GeoFluids 2020 proposed research plan for field studies:
Proposal section 2.3.2: Validate poromechanical predictions with field studies
Example: Document salt-induced pressure and stress effects?
Approach: Work with sponsors and public databases to identify data sets in salt systems and thrust belts to document geomechanical model predictions

## Slide 86: UT GeoFluids 2020 proposed research plan for field studies: Proposal section 2.3.3: Validation of pressure prediction workflows
Validate pressure/stress prediction workflows in field with available data.
Extend pressure-prediction workflows by coupling three-dimensional geomechanical models with velocity data.
Drilling window, s3-u (ppg)
FES
VES
Mud weights calculated from sea floor

## Slide 87
2.4 Deliverables

## Slide 88
Technology transfer
2018 annual meeting Austin: 63 attendees from all 11 companies

## Slide 89
Website

## Slide 90
Website: Presentations

## Slide 91
Website: Publications

## Slide 92
Website: on line databases

## Slide 93
Website:
Software

## Slide 94
The new UT-FAST P3 tool

## Slide 95
Predicting pore pressure using the full stress tensor

## Slide 96
Proposal Section 2.4: Deliverables:
Cuttings Protocol: We will deliver a protocol for on-site (on-rig) cleaning and testing of cuttings. We will provide correlations between liquid limits/clay fraction and stress ratio, friction angle, and undrained strength. This tool will allow quick estimation of least principal stress and strength during drilling.
Salt Pressure-Stress Atlas: We will build an atlas that relates salt geometry to pressure and stress predictions. This atlas will provide insights into qualitatively estimating stress, pressure, and hazardous zones near salt.
Road Map for Intact vs. Resedimented Behavior: We will build a database that compares intact with resedimented behavior.
Online Experimental Database: We will provide an online database containing our experimental measurements for use by the sponsors for internal evaluations.

## Slide 97
Poromechanical Model Results: We will communicate and distribute poromechanical model results in standard industry software format and in excel spreadsheets, so that the insights are more easily applied.
Online Software: We will continue to build online software to communicate the concepts we are developing in UT GeoFluids.
Workflows: We will continue to develop our workflow to couple seismic models with poromechanical models to predict pressure and stress.
Synthetic Seismic Images: We will deliver tools and workflows to generate synthetic seismic datasets from our poromechanical models.
Annual Meetings & Annual Company Visits.
Proposal Section 2.4: Deliverables:

## Slide 98
2.5 Logistics

## Slide 99
Logistics:
First payment in May 2019 ($50,000). Increment at 2%/yr.
No penalty for withdrawing
Members who enter after Year 1 will pay one back year.
Current members will need to sign an amendment
New members will need to sign an agreement that reflects the 2009 proposal and the amendment.

## Slide 100
Outstanding Question for discussion:
Explore stress evolution during production?
Explore pressure/stress in unconventional basins (e.g. Permian Basin)?

## Slide 101: UT GeoFluids experimental publications
Deireh, A., Chang, I.Y., Whittaker, M.L., Weigand, S., Keane,D., Rix, J., Germaine, J.T., Joester, D., and Flemings, P.B., (2017), “Clay Gel Porosity Revisited: the Case Against the Honeycomb Structure,” Applied Clay Science.
Casey, B., Germaine, J.T, Flemings, P.B. and Fahy, B.P., (2017), “In Situ Stress State and Strength in Mudrocks,” J. Geophysical Research: Solid Earth, 121(8), 5611-5623
Adams, A., Nordquist, T.J., Germaine, J.T., and Flemings, P.B. (2016), “Permeability Anisotropy and Resistivity Anisotropy of Mechanically Compressed Mudrocks,” Canadian Geotechnical Journal, 53(9), 1474-1482. 10.1139/cgj-2015-0596
Casey, B., Germaine, J.T., Abdulhadi, N.O., Kontopoulos, N.S., and Jones, C.A., (2015), “Undrained Young’s Modulus of Fine-Grained Soils,” J. Geotechnical and Geoenvironmental Engineering, ASCE, DOI: 10.1061/(ASCE)GT.1943-5606.0001382
Casey, B., Germaine, J.T., Flemings, P.B., and Fahy, B.P. (2015), “Estimating Horizontal Stresses for Mudrocks under One-Dimensional Compression,” Marine and Petroleum Geology, (63), 178-186.
Casey, B, and Germaine, J.T., (2014), “An evaluation of three triaxial systems with results from 0.1 to 100 MPa,” Geotechnical Testing Journal, ASTM, V37, N6
Marjanovic, J. and Germaine, J.T., (2013), “Experimental Study Investigating the Effects of the Setup Conditions on Bender Element Velocity Results,” Geotechnical Testing Journal, 36, (2), GTJ20120131.
Casey, B. A., and Germaine, J.T., (2013), “The Stress Dependence of Shear Strength in Fine-Grained Soils and Correlations with Liquid Limit,” Journal of Geotechnical and Geoenvironmental Engineering, ASCE, 139, (10), 1709-1718.

## Slide 102: UT GeoFluids experimental publications
Casey, B., and Germaine, J.T., (2013), “Liquid Limit as a Predictor of Fine-Grained Soil Strength,” Journal of Geotechnical and Geoenvironmental Engineering, ASCE
Casey, B., Germaine, J.T., Flemings, P.B., Gao, B., Reece, J.S., and Betts, W., (2012), “Liquid Limit as a Predictor of Mudrock Permeability,” Marine and Petroleum Geology, (44), 256-263.
Adams, A., Germaine, J.T., Flemings, P.B., and Day-Stirrat, R., (2013), “Stress Induced Permeability Anisotropy of Resedimented Boston Blue Clay,” Water Resources Research, doi: 10.1002/wrcr.20470
Abdulhadi, N.O., Germaine, J.T, and Whittle, A.J., (2012), “Stress-Dependent Behavior of Saturated Clay,” Canadian Geotechnical Journal, 49, 907-916
Day-Stirrat, R.J., Schleicher, A.M., Schneider, J., Flemings, P.B., Germaine, J.T., and van der Pluijm, B.A., (2011), “Preferred orientation of phyllosilicates: Effects of composition and stress on resedimented mudstone microfabrics,” Journal of Structural Geology, 33 (9) 1347-1358.
Schneider, J., Flemings, P.B., Day-Stirrat, R.J., and Germaine, J.T., (2011), “Insights into pore-scale controls on mudstone permeability through resedimentation experiments,” Geology, 39 (11), 1011-1014.
Abdulhadi, N.O., Germaine, J.T., and Whittle, A.J., (2011), “Thick-Walled Cylinder Testing of Clay for the Study of Wellbore Instability,” Journal of Geotechnical Testing Journal, 34 (6), 766-776.
Abdulhadi, N.O., Germaine, J.T., and Whittle, A.J., (2011), “Experimental Study of Wellbore Instability in Clays,” Journal of Geotechnical and Geoenvironmental Engineering, ASCE, 137 (8), 766-776.

## Slide 103
UT GeoFluids poromechanical publications
Nikolinakou M.A., Heidari M., Flemings P.B., Hudec M.R., 2018. Geomechanical modeling of pore pressure in evolving salt systems, Marine and Petroleum Geology, doi: https://doi.org/10.1016/j.marpetgeo.2018.03.013
Gao, B., Flemings, P., Nikolinakou, M., Saffer, D., Heidari, M., 2018 (online). Mechanics of Fold-and-Thrust Belts Based on Geomechanical Modeling. Journal of Geophysical Research.
Heidari, M., Nikolinakou, M.A., Flemings P.B. (in press). Coupling geomechanical modeling with seismic pressure prediction. Geophysics.
Nikolinakou M.A., Flemings P.B., Heidari M., Hudec M.R. (2018): Stress and pore pressure in mudrocks bounding salt systems; submitted to Rock Mechanics Rock Engineering .
Heidari, M., Nikolinakou M.A., and Flemings, P. B. (2018): “Enhancing Modified Cam Clay Model for large stress range”, 52nd U.S. Rock Mechanics/Geomechanics Symposium, Seattle, WA, June 17-20; Paper # 790..
Nikolinakou M.A., HeidariM., Hudec M.R., and Flemings, P. B. (2018): “ Geomechanical modeling of stress and deformation associated with salt‐sheet advance”, 52nd U.S. Rock Mechanics/Geomechanics Symposium, Seattle, WA, June 17-20; Paper # 637.
Nikolinakou, M. A ., M. Heidari, M. R. Hudec, and P. B. Flemings, 2017, Initiation and growth of salt diapirs in tectonically stable settings: upbuilding and megaflaps, American Association of Petroleum Geologists Bulletin, DOI:10.1306/09021615245.

## Slide 104
UT GeoFluids poromechanical publications
Luo, G., Hudec, M. R., Flemings, P. B., and Nikolinakou, M. A., 2017, Deformation, stress, and pore pressure in an evolving suprasalt basin: Journal of Geophysical Research: Solid Earth, v. 122, no. 7, p. 5663–5690, http://doi.org/10.1002/2016JB013779.
Gao, B., and Flemings, P.B., 2017, Pore pressure within dipping reservoirs in overpressured basins, Marine and Petroleum Geology, 80, 94-111, doi:http://dx.doi.org/10.1016/j.marpetgeo.2016.11.014.
Nikolinakou, M.A., Flemings, P.B., Hudec, M.R., 2016, Modeling of shales in salt-hydrocarbon systems, Rock Mechanics Rock Engineering, v. 49, pp699–705 DOI 10.1007/s00603-015-0863-2.
Heidari, M., M. A. Nikolinakou, M. R. Hudec, and P. B. Flemings, 2016, Geomechanical analysis of a welding salt layer and its effects on adjacent sediments: Tectonophysics, v. 683, p. 172-181, doi http://dx.doi.org/10.1016/j.tecto.2016.06.027.
Heidari, M., M. A. Nikolinakou, P. B. Flemings, and M. R. Hudec, 2016, A simplified stress analysis of rising salt domes: Basin Research, doi 10.1111/bre.12181.
Luo, G., P. B. Flemings, M. R. Hudec, and M. A. Nikolinakou, 2015, The role of pore fluid overpressure in the substrates of advancing salt sheets, ice glaciers, and critical-state wedges, J. Geophys. Res. Solid Earth, 120, 87–105, doi: 10.1002/2014JB011326.

## Slide 105
UT GeoFluids poromechanical publications
Nikolinakou, M.A., Flemings, P.B., Hudec, M.R. (2014a): “Modeling stress evolution around a rising salt diapir”, Journal of Marine and Petroleum Geology, v. 51, pp230-238, doi: http://dx.doi.org/10.1016/j.marpetgeo.2014.07.002.
Nikolinakou, M.A., Hudec, M.R., Flemings, P.B. (2014b): “Comparison of evolutionary and static modeling of stresses around a salt diapir”, Journal of Marine and Petroleum Geology, v. 57, pp537-545, doi: http://dx.doi.org/10.1016/j.marpetgeo.2013.11.021.
Nikolinakou, M.A., Luo, G., Hudec M.R., Flemings P.B. (2012): “Geomechanical Modeling of Stresses Adjacent to Salt Bodies: 2. Poro-Elasto-Plasticity and Coupled Overpressures”, American Association of Petroleum Geologists Bulletin, vol. 96, No1, pp65-85, doi: DOI:10.1306/04111110143.
Luo, G., Nikolinakou, M.A., Hudec M.R., Flemings P.B. (2012): “Geomechanical Modeling of Stresses Adjacent to Salt Bodies: 1. Uncoupled models”, American Association of Petroleum Geologists Bulletin, vol. 96, No1, pp43-64, doi: DOI:10.1306/04111110144.

## Slide 106
UT GeoFluids Field Studies publications
Gao, B., and Flemings, P.B., 2017, Pore pressure within dipping reservoirs in overpressured basins, Marine and Petroleum Geology, 80, 94-111, doi:http://dx.doi.org/10.1016/j.marpetgeo.2016.11.014.
Pinkston, William, 2017, Pore Pressure at the Macondo Well, Mississippi Canyon, Gulf of Mexico, MS dissertation, The University of Texas at Austin, advisor P.B. Flemings
Flemings, P.B., Saffer, D.M., 2018. Pressure and Stress Prediction in the Nankai Accretionary Prism: A Critical State Soil Mechanics Porosity-based approach, Journal of Geophysical Research, doi:10.1002/2017JB015025.
Reilly, M., Flemings, P.B., 2010, Deep Pore Pressures and Seafloor Venting in the Auger Basin, Gulf of Mexico, Basin Research, V. 22, p. 380-397, doi:10.1111/j.1365-2117.2010.00481.
Merrell, M.P., Flemings, P.B., Bowers, G.L., 2014, Subsalt Pressure Prediction in the Miocene Mad Dog Field, Gulf of Mexico, AAPG Bulletin, v. 98, no. 2, p. 315-340, doi:10.1306/06251312156.
Seldon, B., Flemings, P.B., 2005, Reservoir Pressure and Seafloor Venting: Predicting Trap Integrity in a Deepwater Turbidite Reservoir, AAPG Bulletin, v. 89, no. 2, p. 193-209.
Sanford, Jason, 2015, The Cretaceous-Paleogene boundary deposit in the Gulf of Mexico: Oceanic basin response to the Chicxulub impact and Geomechanics of reservoir-scale sand injectites, Panoche Hills, California, MS dissertation, The Unversity of Texas at Austin, advisor P.B. Flemings.

## Slide 107
UT GeoFluids Field Studies publications
Sanford, Jason, 2015, The Cretaceous-Paleogene boundary deposit in the Gulf of Mexico: Oceanic basin response to the Chicxulub impact and Geomechanics of reservoir-scale sand injectites, Panoche Hills, California, MS dissertation, The Unversity of Texas at Austin, advisor P.B. Flemings.
Long, H., Flemings, P.B., Germaine, J.T. and Saffer, D.M., 2011, Consolidation and overpressure near the seafloor in the Ursa Basin, deepwater Gulf of Mexico, Earth Planet. Sci. Lett., 305, 11-20
Flemings, P.B., Long, H., Dugan, B., Germaine, J., John, C., Behrmann, J.H., Sawyer, D., and Expedition 308 Scientists, 2008, Erratum to "Pore pressure penetrometers document high overpressure near the seafloor where multiple submarine landslides have occurred on the continental slope, offshore Louisiana, Gulf of Mexico" [Earth and Planetary Science Letters 269/3-4 (2008) 309-32, Earth and Planetary Science Letters, doi: 10.1016/j.epsl.2008.06.027.
Flemings P.B., Stump, B.B., Finkbeiner, T., Zoback, M., 2002, Flow Focusing in Overpressured Sandstones: Theory, Observations, and Applications , American Journal of Science, v. 302, p. 827-855.
Lupa, J.A., Flemings, P.B., Tennant, S., 2002, Pressure and Trap Integrity in the Deepwater Gulf of Mexico, The Leading Edge, V. 21, no. 1, p. 84-87.
Finkbeiner, T., Zoback, M., Stump B.B., Flemings, P.B., 2001, Stress, Pore Pressure, and Dynamically Constrained Hydrocarbon Columns in the South Eugene Island 330 Field, Gulf of Mexico, American Association of Petroleum Geologists Bulletin, V. 85, no. 6, p. 1007-1031.